## Slide 1
Time in Navigation
NN220-11
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation– Updated May 2023
SEANAV I United States Naval Academy

## Slide 2
References
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The American Practical Navigator, Pub. No. 9, Bowditch, VOL. 1, 2019 Edition -Surface Ship Navigation Department Organizations and Regulations Manual (NAVDORM), COMNAVSURFPAC/COMNAVAIRPAC/COMNAVAIRLANT/COMNAVSURFLANT INSTRUCTION 3530.4 series

## Slide 3
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 – UNDERSTAND time as a function of the Earth’s rotation around the sun. 2 - DEFINE Apparent Time and Mean Solar Time. 3 - UNDERSTAND Universal Time (GMT or Greenwich Meridian) and its application to time. 4 - UNDERSTAND Longitude Arc and arc to time conversion. 5 - UNDERSTAND the purpose of the International Date Line. 6 - DEFINE Zone Time (ZT) and Zone Description (ZD). 7 - DETERMINE zone time and make zone time conversions. 8 - UNDERSTAND the time zones, their division and the military’s standard use of Zulu time. 9 - DEFINE Speed of Advance (SOA), Estimated Time of Arrival (ETA), and Estimated Time of Departure (ETD). 10 - DETERMINE the distance between ports using PUB 151. 11 - COMPUTE SOA, ETA, ETD and apply zone time conversion required for voyage planning.

## Slide 4
Time Zones Explained
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Geography Lesson: Time Zones Explained | Twig - YouTube

## Slide 5
The Earth’s Rotation
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The Earth’s rotation on her axis presents the Sun and other Celestial Bodies to appear to proceed across the sky from East to West.
-If we measure the time interval between the transits between these celestial bodies, we would be measuring a period of the Earth’s rotation.
-The Earth’s rotation is a navigator’s standard of time.
-The Earth completes a full rotation (360°) over the course of a day, or approximately 24 hours
(actually 23 hours and 56 minutes).

## Slide 6
The Earth’s Rotation
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-This means that different parts of the world are in different times of the day, depending on where they are on Earth and the rotation of the sun.

## Slide 7
How To Measure Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Most of us just use the clocks installed into our phones and smart watches.
-There is a mathematical approach to how time is measured and observed.
-The fundamentals are based on Apparent Solar Time, Mean Solar Time and the Equation of Time.

## Slide 8
Apparent Solar Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Apparent Solar Time is the time we would have if a perfectly constructed and calibrated sun dial would read at a given location, based on the position of the Sun in the sky. -Seems like the ideal time to use, however it is not a uniform scale. -The apparent Sun crosses the sky at slightly different rates throughout the year. -This means that apparent time runs fast with regard to a constant time scale. It is not ideal for timekeeping. -So what do we do?

## Slide 9
Mean Solar Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-To create a uniform scale, we use mathematics to find the place where the sun should be if it moved at a constant rate throughout the sky, regardless of the time of year.
-Called “Fictitious” Mean Sun.
-Never more than 4° East or West of the actual Sun.
-Mean Solar Time is defined like Apparent Solar Time, but we use the fictitious position of the sun.
-Since we can’t see the fictitious sun, we use the Equation of Time, or the difference between Mean Solar Time and Apparent Solar Time on any given day.

## Slide 10
Equation of Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-By knowing our Apparent Solar Time and the Equation of Time, we can find Mean Solar Time. -The equation of time can vary depending on the time of year. In mid-February the value is almost -14 minutes 13 seconds and + 16 minutes and 26 seconds in early November. -This information can be found in the Nautical Almanac. -Apparent Time = Mean Time +/- Equation of Time.

## Slide 11
Example
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
The Gray highlight means it is a subtracted time!

## Slide 12
Create a Foundation
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Equipped with the information needed to determine Mean Solar Time, we can determine the time around the world based on the fictitious movement of the sun. -This allows a more consistent method of measuring time, not accounting for the shifts of the apparent sun’s movement throughout the year. -A reference point is needed to be created to based time around. -That reference is the Greenwich Meridian, or the Prime Meridian.

## Slide 13
Greenwich Mean Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Greenwich Mean Time (GMT) is widely used as the mean solar time at zero longitude, or the Prime Meridian.
-Based in Greenwich, UK.
-Called Zulu (Z), GMT, UT, UTC, and UT1. They all mean the same thing.
-Is the generic reference to the timescale that approximates mean diurnal motion of the fictitious sun.
-In navigation, Zulu is the standard to which we base all the time zones of the world.

## Slide 14
Time and Longitude Arc
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The navigator may be required to convert the measure of longitude arc to time or vice versa. -Remember that longitude is a function of time. -Mean Solar Day = one complete rotation of the Earth or 360°. -One rotation of the Earth = one 24 hour period. -One 24 hour period = 1440 minutes. -60 minutes =15° of longitude. 15° = one timezone! (with some exceptions including the International Date Line)

## Slide 15
Time Zones
Z
0
O
+ 2
N
+ 1
A
- 1
B
- 2
7.5°
7.5°
15°
007.5°E
007.5°W
022.5°E
022.5 °W
030o W
037.5 °W
037.5°E
- 23 of time zones are 15° wide.
030o E
015o W
015o E
Prime Meridian
Subtract(-) 1 Hour
Add(+) 1 Hour
Subtract(-) Hours
Add(+) Hours

## Slide 16
There are 25 of time zones all around the world.
“M” ,”Y” ; the same time, but different days
International Date Line; located at 180°
West of Z (N-Y) is “+”
East of Z (A-M) is “-”
Z
L
K
C
H
I
G
F
E
B
A
M
D
-1
-2
-3
-4
-5
-6
-7
-8
-9
-10
-11
-12
U
T
V
W
X
P
Q
S
R
O
Y
N
+1
+2
+4
+7
+5
+11
+6
+10
+9
+8
+3
+12
The Sun travels 360° in 24 hours.
“J” ; missing!! Refers to current local time of
the observer
“Z” ;the reference for all others

## Slide 17
Time Zones
U
T
V
W
X
P
Q
S
R
O
Y
N
+1
+2
+4
+7
+5
+11
+6
+10
+9
+8
+3
Z
L
K
C
H
I
G
F
E
B
A
M
D
-1
-2
-3
-4
-5
-6
-7
-8
-9
-10
-11
Z
0
O
+ 2
N
+ 1
A
- 1
B
- 2
7.5°
7.5°
15°
007.5°E
007.5°W
022.5°E
022.5 °W
030o W
037.5 °W
037.5°E
- 23 of time zones are 15° wide.
030o E
015o W
015o E
Prime Meridian
Subtract(-) 1 Hour
Add(+) 1 Hour

## Slide 18
Time Zones
U
T
V
W
X
P
Q
S
R
O
Y
N
+1
+2
+4
+7
+5
+11
+6
+10
+9
+8
+3
Z
L
K
C
H
I
G
F
E
B
A
M
D
-1
-2
-3
-4
-5
-6
-7
-8
-9
-10
-11
- 02 of time zones are 7.5° wide Y and M.
M
-12
K
-10
L
-11
X
+11
W
+10
7.5°
7.5°
15°
Add(+) 1 Day
Subtract(-) 1 Day
International Date Line
172.5°W
172.5°E
157.5°W
157.5°E
150o E
142.5° E
142.5°W
150o W
165o E
165o W
Y
+12
180o

## Slide 19
Determine Time Zones Geographically
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
  If you did not know the local time zone of a specific location what could you do?
    Longitude derives time zone.
  Example: San Diego - 117° 10’ W
  Convert longitude into degrees 10’ 1° = .167° + 117°= 117.167°W
  60’
  Covert degrees into hours 117.167° 1 hr = 7.8 hrs West
  15°
  Round to nearest whole number 8 hrs western hemisphere... +8U (it is + because it is in the West)

## Slide 20
Zone Description
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Your ZD is used to find your time zone in reference to Z (GMT). -In Annapolis we are +5R. -We would take our local time, add 5 hours, and we would know what time GMT would be at. -ZD’s N(+1) to Y(+12) (WESTward) and A(-1) to M(-12) (EASTward) – except “J”

## Slide 21
Zone Description
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Each time zone will have a letter of the alphabet and a number assigned to it. -The exception for the alphabet is “J”, which not a timezone. -These letters and numbers are called your Zone Description (ZD). -In Annapolis, our ZD is +5R

## Slide 22
The International Date Line
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Since time accumulates differently depending on whether you are traveling East or West, a traveler circling the Earth will lose or gain a day. -To provide a starting point, a meridian (sort of…) was drawn and fixed by an informal agreement, called the International Date Line. -The IDL separates two consecutive calendar days. -You lose a day traveling east across the IDL. -You gain a day traveling west across the IDL.

## Slide 23
Time Zones
San Diego
Manila
“If it’s SUNday in SAN Diego,
it’s MONday in MANilla”
Add(+) 1 Day
Subtract(-) 1 Day

## Slide 24: Practice
24
Q1: What is the complete Zone Description for 075o 00’00”W ?
075o 00’00”W / 15° =
5
+5R

## Slide 25: Practice
25
Q3: What is the complete Zone Description for 127 o 35’00”W ?
157 o 40’00”E / 15° =
-11L
11
= 10.51...
Round up or down based on 0.5
Q2: What is the complete Zone Description for 127 o 00’00”W ?
Q3: What is the complete Zone Description for 157 o 40’00”E ?
157.66 o E / 15°
40 ‘ / 60 = 0.6666…
157°40’E
157.66…°E

## Slide 26
U
T
V
W
X
P
Q
S
R
O
Y
N
+1
+2
+4
+7
+5
+11
+6
+10
+9
+8
+3
Z
L
K
C
H
I
G
F
E
B
A
M
D
-1
-2
-3
-4
-5
-6
-7
-8
-9
-10
-11
The Sun daily travels westbound from IDL
261530R
261230U
San Diego
(Time zone = U)
Annapolis
(Time zone = R)
Tokyo
(Time zone = I)
Greenwich
270530i
262030Z
270830M
260830Y
-12
+12

## Slide 27: Practice
27
Q4: If it is 0800 in Annapolis, MD (+5R) on 26 February 2018, what time is that in Perth, Australia (-8H) ?
Time zone “H” is ahead of “R” for
262100HFEB18
2100, 26 February 2018 (-8H)
+13 hours
0800, 26 February 2018
+) 13 (hours)
13 hours.

## Slide 28: Practice
28
Q5: If it is 0800 in Annapolis, MD (+5R) on 26 February 2018, what time is that in Pearl Harbor, HI (+10W) ?
Time zone “W” is behind “R” for
260300WFEB18
0300, 26 February 2018 (+10W)
-5 hours
0800, 26 February 2018
-) 5 (hours)
5 hours.

## Slide 29
Convert the Longitude to Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Our longitude at USNA is 076° 29’ 00’’. -Arc to time conversion…convert seconds and minutes to decimals. -29’/60 (60 minutes in an hour) = .4333333. -Longitude is converted to 076.4333333°. -076.4333333°/15 (number of degrees in an hour) = 5.096 hours. -USNA is 5 hours and 5 minutes and 56 seconds away from the base longitude of the Prime Meridian!

## Slide 30: Arc to Time Conversion
ARC | Time
This information was essential to early navigation!
By knowing the time at your home port and the time where you are (based on the Sun’s position), you could calculate how many degrees of longitude separated you and therefore determine your location east or west of your origin (or the prime meridian).
The Sun goes around the Earth per 24 hours.
1/15
1/15
1/60
1/60
15°
1°
1’
1 hr (60min)
4
4 sec
(60’)
min

## Slide 31: Practice
31
Q7: If sunrise occurs at 0620 in Boston, MA (071°05’W),
what time will the sunrise in Annapolis, MD (076°28’W)?
Difference between Boston and Annapolis is…
5°23’
5° = 5(°)* 4(min)
= 20 min
23’ = 23(’) * 4(sec)
= 92 seconds
= 1 min 32 sec
21 min 32 sec
Annapolis is 21 min 32sec BEHIND Boston.
06-20-00 + 0-21-32 =
06-41-32
31
Boston
ARC | Time
15°
1°
1’
1 hr (60min)
4
4 sec
(60’)
min
Annapolis
Boston
21 min 32 sec
076°28’W
-) 071°05’W
5°23’W

## Slide 33
Determine Time Zones Geographically
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
  This method is not always accurate.
  Due to social/political/economic reasons, some countries will not honor their geographic time zone.
  Iceland goes by Z and should be +1N.
  Iran goes by 3.5 hours….when everyone is on the hour they are on the half hour!

## Slide 35
Washington DC
+5R
West is Best
Add 5hrs to return to Z
1200R = 1700Z
Bahrain
-4D
East is Least
Minus 4hrs to return to Z
2100D = 1700Z
Each Timezone = 15°Longitude
Except M / Y = 7.5°each (15°total)

## Slide 36
Daylight’s Savings Time
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Daylight Savings. As a result of the early rising of the sun in summer, a certain amount of daylight would be lost if time zones were not adjusted. -To avoid this loss, it is customary to adopt the time of the next adjacent zone to the east during a portion of the year. -This results in sunrise and sunset occurring one hour later by the clock. -In the summer months, we “Spring forward” one time zone towards Zulu. -In the winter months, we “Fall back” one time zone from Zulu. -Legal times for countries may differ to align with bigger neighbors!

## Slide 37
Military’s Standard Use
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The U.S. Military makes standard use of Z time. -Since forces are dispersed around the world, it’s easier to use the base reference time. -You have seen it before….

## Slide 39
Let’s Practice
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The concept of time in navigation is especially critical as we transit vast oceans and cross multiple time zones. -Let’s work a hypothetical scenario and use all the tools together.

## Slide 41
Let’s Practice
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Our DESRON has ordered us to sea. -We were presented with a time to depart Pearl Harbor, HI and a time to arrive in San Diego, CA. -This is common tasking. -Our time to depart is called our Estimated Time of Departure (ETD) and our arrival time is called our Estimated Time of Arrival (ETA). -Since we are given our ETA and ETD, we must determine our Speed of Advance (SOA) or how fast we would need to go to get to our destination on time.

## Slide 42
Prepare the Voyage Plan
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1. Determine port of departure/arrival, date of departure/arrival (Done!) 2. Determine Chart and Publication requirements 3. Determine Distance and SOA 4. Plan the passage

## Slide 43
Determine Charts and Publication Requirements
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Identify that you have the most recent DNC or ENC libraries to support the transit. -Apply the VDU corrections and ensure that both your charts and navigation equipment is aligned to WGS-84. -Do your research on the voyage using such publications as PUB 151, Coast Pilots, Sailing Directions, Pilot Charts, etc.

## Slide 44
Digital Nautical Chart - HOME PAGE (nga.mil)

## Slide 45
Digital Nautical Chart - HOME PAGE (nga.mil)

## Slide 46
Chart Locator (noaa.gov)

## Slide 48
Page 95
Page 96
ALWAYS START AT PORT OF DEPARTURE!

## Slide 49
Example: Determining the distance from Norfolk, VA to Al Manamah, Bahrain by using Junction Points

## Slide 50
Prepare the Voyage Plan
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1. Determine port of departure/arrival, date of departure/arrival (Done!) 2. Determine Chart and Publication requirements (Done!) 3. Determine Distance and SOA 4. Plan the passage

## Slide 51
Time, Speed, Distance
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Time, Speed, and Distance is critical in building navigation plans. Distance (NM) = Time (HRS) X Speed (KTS) -If you have two of these, you can find the other. -In our example, we are given the time requirements and we can find the distance from PUB 151, so we are solving for the SOA needed. -When working these problems, read the instructions carefully to determine what needs to be solved.

## Slide 52
Determine Distance and SOA
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Based on PUB 151, the distance between Pearl Harbor and San Diego is 2,285NM. -ETD is 011200WSEP21 -ETA is 101200USEP21 -Convert the time zones to ZULU. -ETD = 011200WSEP21 (+10W) = 012200ZSEP21 -ETA = 101200USEP21 (+8U) = 102000ZSEP21

## Slide 53
Determine Distance and SOA
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Difference between ETD and ETA will give you TOTAL TRANSIT TIME. -012200ZSEP21 to 102000ZSEP21 = 8 days and 22 hours -Convert to hours = (24 x 8) = 22 = 214 hours -SOA = 2285NM / 214 Hours = 10.67 Knots (We would round up to 11 knots)

## Slide 54
Prepare the Voyage Plan
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1. Determine port of departure/arrival, date of departure/arrival (Done!) 2. Determine Chart and Publication requirements (Done!) 3. Determine Distance and SOA (Done!) 4. Plan the passage

## Slide 57
Divide route into legs, no more than 350-400 NM each.
Change each of the legs from GCs to RLs.

## Slide 58
155◦
150◦
145◦
140◦
135◦
130◦
125◦
120◦
160◦
45◦
40◦
35◦
30◦
25◦
20◦
50◦
Essentially, you’ve broken up a Great Circle track into smaller legs using Rhumb Lines to form a Composite Track.
This allows for steadying courses, while still driving the shortest distance.
Rhumb Line 2280 NM
Composite Track 2270 NM

## Slide 59
Prepare the Voyage Plan
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1. Determine port of departure/arrival, date of departure/arrival (Done!) 2. Determine Chart and Publication requirements (Done!) 3. Determine Distance and SOA (Done!) 4. Plan the passage (Done!)

## Slide 60
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 – UNDERSTAND time as a function of the Earth’s rotation around the sun. 2 - DEFINE Apparent Time and Mean Solar Time. 3 - UNDERSTAND Universal Time (GMT or Greenwich Meridian) and its application to time. 4 - UNDERSTAND Longitude Arc and arc to time conversion. 5 - UNDERSTAND the purpose of the International Date Line. 6 - DEFINE Zone Time (ZT) and Zone Description (ZD). 7 - DETERMINE zone time and make zone time conversions. 8 - UNDERSTAND the time zones, their division and the military’s standard use of Zulu time. 9 - DEFINE Speed of Advance (SOA), Estimated Time of Arrival (ETA), and Estimated Time of Departure (ETD). 10 - DETERMINE the distance between ports using PUB 151. 11 - COMPUTE SOA, ETA, ETD and apply zone time conversion required for voyage planning.

## Slide 61
Questions?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy